## Slide 1: EDES 301 Digital Stethoscope Proposal
Daniel Gutierrez
10/04/2025

## Slide 2: Background Information
This project aims to develop an electronic stethoscope capable of digitally capturing and analyzing heart sounds. A condenser microphone will be integrated into the stethoscope to record auscultation signals, which are transmitted wirelessly via a Bluetooth interface and displayed in a serial terminal window for analysis. The system will incorporate physiologically relevant metrics, including frequency thresholds associated with normal and abnormal heart sounds, to automatically flag potential outliers that may indicate underlying health complications. Beyond diagnostic support, this project seeks to provide users with an accessible means to understand and interpret their own cardiac sounds, bridging traditional auscultation techniques with modern digital health monitoring
Link to Existing Project
While this project establishes a solid foundation for the circuitry behind an electronic stethoscope, additional noise filtering and signal amplification will likely be required to achieve the desired resolution for accurate data analysis. Furthermore, rather than simply displaying the recorded data, the project aims to provide users with meaningful insights by identifying and flagging outlier heart sounds based on established physiological reference values.

## Slide 3: System Block Diagram
Microphone + Stethoscope
Capacitor Filter
Band Pass Filter
Audio Amplifier
Required Audio Range (20Hz-1300Hz) is only passed.
ADC
Micro Controller
Output to the device
(speaker / PC / Bluetooth Module)
Display LED Indicator
(GPIO)
Analog
Analog
Analog
Digital via SPI / I^2C
I^2C/SPI

## Slide 4: Power Block Diagram
Battery / USB Power
Power Regulation
(5V → 3.3V)
Analog Section (Mic, Filters, Amplifiers)
V=3.3V
I= 0.5-0.35 mA
Digital Section
(ADC & MCU)
V=3.3V
I=0.6-25 mA
Peripherals & Display
V=3.3V
I=1-100 mA

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
1- USB Bluetooth | Yes | $9.99
1- Op-Amp | No | 
1- Adjustable voltage adapter (1A) | Yes | $11.99
1- Breadboard | No | 
2 - 1K resistor | No | 
1 - 3.3K Resistor | No | 
3 – 10K Resistor | No | 
1 – 100K Resistor | No | 
1 - 470nF Capacitor | No | 
1 – 2.2μF Capacitor | No | 
1- ADC | Yes | $11.88
1- Stethoscope | No | 
1- MEMS microphone | No |